FL-200 FLUID GRANULATOR DRYER

Application

The machine is mainly used for the operation of mixing, granulating, drying and coating of granule, etc. It can widely used in tablet granule, instant coffee drink, condiment, etc. The machine is designed accordance with JB20014-2004.

Features

- Mixing, granulating, drying in one step.

- Adopted double chamber filtering bag system, removing dust clearly.

- Adopted multi-fluid nozzle, which guarantee the formed granule is uniform, the powder proportion is low.

- It can choose anti-explosion design.

- The machine design and manufactured according GMP standard.

| Specification | 5 | 15 | 30 | 45 | 60 | 90 | 120 | 150 | 200 | 300 | 500 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Container Volume (L) | 22 | 45 | 100 | 155 | 220 | 300 | 420 | 550 | 670 | 1000 | 1500 |
| Output Capacity (KG/batch) | 5 | 15 | 30 | 45 | 60 | 90 | 120 | 150 | 200 | 300 | 500 |
| Steam | Pressure (Mpa) | 0.4-0.6 |
|  | Consumption(KG/h) | 18 | 35 | 60 | 99 | 120 | 130 | 140 | 161 | 180 | 310 | 400 |
| Fan Power (KW) | 4 | 4 | 5.5 | 7.5 | 11 | 15 | 18.5 | 22 | 22 | 30 | 45 |
| Heating Power (KW) | 6 | 9 | / | / | / | / | / | / | / | / | / |
| Noise (dB) | No More than 75 dB |
| Air | Pressure (Mpa) | 0.6 |
|  | Consumption (m³/min) | 0.3 | 0.6 | 0.6 | 0.6 | 0.9 | 0.9 | 0.9 | 0.9 | 1.1 | 1.3 | 1.5 |
| Overall Size (mm) | H1 | 2600 | 2100 | 2250 | 2250 | 2850 | 2850 | 2850 | 3050 | 3300 | 3500 | 3850 |
|  | H2 |  | 250 | 320 | 420 | 490 | 540 | 590 | 640 | 690 | 790 | 890 |
|  | H3 |  | 1900 | 2050 | 2050 | 2600 | 2600 | 2600 | 2600 | 3000 | 3280 | 3630 |
|  | B1 | 740 | 1010 | 1160 | 1320 | 1460 | 1560 | 1660 | 1760 | 1860 | 2060 | 2260 |
|  | B2 | 1500 | 1800 | 2060 | 2460 | 2660 | 2800 | 3060 | 3260 | 3660 | 4060 |  |
|  | Φ | 400 | 550 | 700 | 860 | 1000 | 1100 | 1200 | 1300 | 1400 | 1600 | 1800 |
|  | Φ2 | 180 | 180 | 250 | 250 | 280 | 280 | 280 | 315 | 315 | 355 | 385 |
|  | L | 1000 | 1100 | 1250 | 1530 | 1530 | 1530 | 1650 | 1650 | 1650 | 1750 | 1850 |

Machine Part List

| No. | Part Name | Content | Specification | Manufacture |
| --- | --- | --- | --- | --- |
| 1 | Machine System | Filtering Chamber: Filtering Dust Collecting System; | SUS304 | Own Factory |
|  |  | Expand Chamber: 3 Spray Gun |  |  |
|  |  | Trolley 1 Set |  |  |
|  |  | Top Area: Double Cylinder and Air Sac Sealing Type |  |  |
|  |  | Air Inlet Chamber: Water Outlet; Air Inlet Regulated |  |  |
|  |  | Main Machine |  |  |
|  |  | Main Machine Sealing: Silicon Rubber |  |  |
|  |  | Temperature: Air Inlet & Outlet |  |  |
| 2 | Air Heating System | Radiator | 145m² | Own Factory |
|  |  | Material | SUS304 | China |
| 3 | Air Filtering System | Primary Filter | Screen & Nonwovens | Own Factory |
|  |  | Cover | SUS304 | Own Factory |
|  |  | High Efficient Filter | 100,000 Level Air Inlet | Taibo China |
| 4 | Air Outlet System | Induced Draft Fan | 30W | Huasheng China |
|  |  | Silencer | Q235 Noise Less than 70dB | Own Factory |
|  |  | Dust Exhausting Pipe | SUS304 | Own Factory |
|  |  | Air Exhausting Pipe | Q235 | Own Factory |
| 5 | Atomization System | Liquid Sprayer | SUS304 | Own Factory |
|  |  | Liquid Trolley | 300L, SUS304 | Own Factory |
|  |  | Liquid Pump | Peristaltic Pump | China |
| 6 | Electronic Control System | Electronic Box Cover | Painted | Own Factory |
|  |  | Operating System | HMI (Touch Screen) | Siemens |
|  |  | Control System | PLC | Siemens |
|  |  | Electronic List | Air Breaker, Relay, Contactor | China |
|  |  | Pneumatic List | Cylinder | Airtac Taiwan |
|  |  | Indicating Instrument | Ampere Meter, Volmeter, Temperature Controller | China |
| 7 | Filter Bag |  | Antistatic | Own Factory |
| 8 | Sight Glass | Stalinite |  | Own Factory |